## Slide 1
SLAC Control Interface (SACI Slave)
32 bit Data Bus
12 bit Address
7 bit Command
CClk
EXEC
Ack
General Purpose
for every SLAC ASIC
CMD Unit
G Registers
16 bit Data Bus
12 bit Address Bus
Row Registers
PIPO with
Read back
Column Registers
Pix Registers
Epix Commands (partial):
ePix Control Interface
R/W
RstL
saciClk
saciCmd
saciRsp
saciSelL

## Slide 2: SLAC ASIC Control Interface (SACI)
Motivation
  Need simple serial interface to ASICs for configuring registers and sending commands.
Standard Options Not a Great Fit
  SPI: No backpressure. No way for ASIC to signal that it is done with a command or ready for new data. Requires polling.
  I2C: Backpressure possible through clock stretching, but complex protocol and implementation.

## Slide 3: SACI Features
Master/Slave Serial Interface
4 Signals
  3 shared: saciClk, saciCmd, saciRsp
  1 dedicated select line per slave: saciSelL
Allows multiple slaves on same SACI bus. (Similar to SPI.)
Serial data transmitted on rising edge of clock and sampled on falling edge. MSB first.
Toggling saciSelL resets Slave state machine in case of lockup.

## Slide 4: SACI Writes
Master lowers saciSelL
Master sends Start Bit, Write Bit, Command, Address and Data
Slave responds with Start Bit, Write bit, Command and Address
Master optionally raises saciSelL when done.

## Slide 5: SACI Reads
Master lowers saciSelL
Master sends Start Bit, Read Bit, Command and Address
Slave responds with Start Bit, Write bit, Command, Address and Data
Master optionally raises saciSelL when done.

## Slide 6: SACI Status
VHDL Coding (Master and Slave) – Done
Digital Simulation – Passed
Synthesis and Layout (Slave) - Done
Analog (transistor level) Simulation – Passed
Stats
  320 Standard Cells
  98.52 µm x 540.20 µm